## Slide 1: Best Practices to Reduce Your Risk of Developing a Cumulative Trauma Injury
Special Emphasis on Employees Who are Young or Newly Hired

## Slide 2: Disclaimer
This material was produced under grant number SH-99053-SH0 from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government.

## Slide 3: Training Topics Reducing Risk of Cumulative Trauma
Why focus on young and newly hired employees?
What causes cumulative trauma, pain, and injury?
How to keep yourself safe and healthy, especially if you are young or a new hire

## Slide 4: Why Focus on Young and Newly Hired Employees?
Reasons for Training

## Slide 5: Who is Considered a Young Employee?
Usually defined as up to 25 years old
Chart: Age Range of Typical Working Population
| 18 | 19-20 | 21-25 | 26-30 | 31-35 | 36-40 | 41-45 | 46-50 | 51-55 | 56-60 | 61-65 | 66-70 | 71-75
Series 1 | 18 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75

## Slide 6: Who is Considered a “New” Employee?
Usually defined as on the job for less than one year
Represents about 20% of the workforce*
* Bureau of Labor Statistics, 2020
Chart: 
| <12 months | 1-2 years | 2 years | 3-4 years | 5-9 years | 10-14 years | 15-19 years | 20+ years
Series 1 | 0.204 | 0.068 | 0.056 | 0.183 | 0.199 | 0.11 | 0.068 | 0.113

## Slide 7: Young Employees are More Likely to Get Injured
“If you’re under 25, you’re more likely to get injured on the job than if you’re over 25.”
More than 50% of accidents involving younger workers occur during the first six months on job

## Slide 8: Why are Young Employees More Likely to Get Injured?
Work-related reasons
  Lack of training and work experience
  Not prepared for job’s physical demands
  More likely to be given riskier jobs
  Misunderstand or are unaware of employee rights

## Slide 9: Why are Young Employees More Likely to Get Injured?
Individual perceptions and attitudes
  Feel invincible
  More likely to take risks or do activities without knowing the consequences
  Less-motivated to find out if an activity is risky
  More easily distracted
  Hesitant to ask questions
L

## Slide 10: Newly Hired Employees are More Likely to Get Injured
Questions: Which new hires are more likely to get injured?
On job for <1 month | or | On job for 1+ years
Males | or | Females
Young employees | or | Older employees
Recent immigrants | or | Established immigrants

## Slide 11: Newly Hired Employees are More Likely to Get Injured
Answers: Which new hires are more likely to get injured?
On job for <1 month | or | On job for 1+ years
Males | or | Females
Young employees | or | Older employees
Recent immigrants | or | Established immigrants
4x!

## Slide 12: Why are Newly Hired Employees More Likely to Get Injured?
Not yet adjusted to the demands of the job
Not yet learned how to do job in a way that lowers physical stress on the body
More likely to develop symptoms of discomfort
L

## Slide 13: What Can Cause Cumulative Trauma, Pain, or Injury?
Understanding how Injuries Occur

## Slide 14: What are Cumulative Trauma Injuries?
Acute injuries can occur following a single high-impact event
vs.
Cumulative trauma injuries build up over time
Examples:
Broken Bone
Laceration
Examples:
Elbow Soreness
Back Pain
Focus of this training
L

## Slide 15: What Can Cause Cumulative Trauma, Pain, or Injury?
Lifting heavy weight or exerting high forces
Examples:
Pushing or Pulling
Exerting Strong Grips
Lifting or Carrying
L

## Slide 16: What Can Cause Cumulative Trauma, Pain, or Injury?
Lifting heavy weight or exerting high forces
This is a risk factor because:
Muscles generate the effort we need to perform a task
The amount of effort needed depends on:
  The amount of weight / force handled, and
  The way that the weight / force exerted
Muscle effort is usually much greater than the weight / force needed for the task
Even small increases in weight / force or the reach to perform a task greatly increases the effort required
Examples:
Far from Body
Muscle Effort
Light
Heavy
Muscle Effort
Close to Body
Muscle Effort
Close to Body
Light

## Slide 17: What Can Cause Cumulative Trauma, Pain, or Injury?
Lifting heavy weight or exerting high forces
Examples:
15#
20#
40#
Lifting 40 lbs. close to the body
Lifting 20 lbs. mid-way from the body
Lifting 15 lbs. at arm’s length from the body
These lifting tasks each put about the same amount of stress on the back
This is a risk factor because:
Muscles generate the effort we need to perform a task
The amount of effort needed depends on:
  The amount of weight / force handled, and
  The way that the weight / force exerted
Muscle effort is usually much greater than the weight / force needed for the task
Even small increases in weight / force or the reach to perform a task greatly increases the effort required

## Slide 18: What Can Cause Cumulative Trauma, Pain, or Injury?
Working in awkward body postures
Examples:
Reaching Overhead
Bending Wrists
Bending Forward

## Slide 19: What Can Cause Cumulative Trauma, Pain, or Injury?
Working in awkward body postures
Amount of muscle strength:
88%
83%
75%
Shoulders
Wrists
This is a risk factor because:
Muscles become weaker as postures become more awkward
Examples:
77%
100%
93%
60%
100%

## Slide 20: What Can Cause Cumulative Trauma, Pain, or Injury?
Repetitively using the same body part
Examples:
Constant Reaching
Rapid Use of Hands & Wrists
Frequent Lifting

## Slide 21: What Can Cause Cumulative Trauma, Pain, or Injury?
Repetitively using the same body part
Chart: Work and Rest Periods of a Job, Over Time
 | 0.001 | 0.001 | 0.001 | 0.001
Chart: Work and Rest Periods of a Job, Over Time
 | 0.001 | 0.001 | 0.001 | 0.001 | 0.001 | 0.001 | 0.001 | 0.001
Amount of cumulative trauma that does not lead to injury
Work Demands < Tolerance
This is a risk factor because:
Over a period of time, the body has less ability to withstand the demands of the job if there is not enough recovery time
Work Demands < Tolerance
Amount of cumulative trauma that does not lead to injury
Work Demands > Tolerance

## Slide 22: What are Symptoms of Cumulative Trauma?
Indications of Wear and Tear on the Body

## Slide 23: Symptoms of Cumulative Trauma Muscles
Symptoms
  Weakness, fatigue
  Pain, tenderness
  Spasms
Likely locations:
There is a lot of blood flow to our muscles, so they can recover from injury very quickly
Muscles generate force when they contract
Back
Neck

## Slide 24: Symptoms of Cumulative Trauma Tendons
Symptoms
  Dull ache that doesn’t go away
  Swelling, tenderness
  Discomfort when moving in specific ways
Likely locations:
There is not much blood flow that flows to our tendons, so they can take a long time to recover
Tendons connect all muscles to bones
Shoulder
Elbow
Knee

## Slide 25: Symptoms of Cumulative Trauma Nerves (example: carpal tunnel syndrome)
Signs of initial trauma
  Numbness and tingling in the hands
  Pain at night
Signs of longer-term trauma
  Weakness
  Problems holding objects
Likely locations:
Nerves send sensations and impulses through the body
Hand & Wrist

## Slide 26: Symptoms of Cumulative Trauma Discs in the Back
Initial trauma
  None! (nothing can be felt when damage first occurs)
Longer-term trauma
  Disc damage affects nerves
    Pain going down the leg
    Numbness, tingling
L
Spinal Discs are the “shock absorbers” between vertebrae

## Slide 27: How Do You Reduce Your Risk of Cumulative Trauma?
Approaches to Protect Yourself from Injury

## Slide 28: Lowering Cumulative Trauma Risk Reduce Muscle Effort & Stress on Body
Examples:
  Get your body as close to the load as possible before picking it up
“Lift with your legs, not your back” is not a good strategy if your knees cause you to lift with the load further away from your body
When possible, straddle the load so that you can lift and handle it closer to your body

## Slide 29: Lowering Cumulative Trauma Risk Reduce Muscle Effort & Stress on Body
Examples:
  Carry items in front of the body
  When possible, balance items handled between sides of the body
  Ask for help when lifting heavy objects
L
L
Allows both sides of the body to equally support the load
Allows both sides of the body to equally support the load
Divides effort between individuals

## Slide 30: Lowering Cumulative Trauma Risk Reduce Muscle Effort & Stress on Body
Examples:
Get your body as close to the load as possible before picking it up
For heavy loads, make more trips with less weight, when possible
Less reaching to pick up a load is safer for the back and shoulders
This practice is nearly always safer for the back

## Slide 31: Lowering Cumulative Trauma Risk Work in Stronger Body Postures
Examples:
  Adjust the height of your work
  Adjust the position of your work
Be creative in finding ways to work while standing in an upright position
Angle your work to reduce wrist bending

## Slide 32: Lowering Cumulative Trauma Risk Work in Stronger Body Postures
Examples:
  Push wheeled containers rather than pull them
  Arrange most-used items to be within arm’s length
Allows both sides of the body to equally exert the effort needed
Reduces over-reaching and stress on the shoulders

## Slide 33: Lowering Cumulative Trauma Risk Recover from Repetitive Tasks during Work
Periodically do simple repetitive activities with your non-dominant hand
Provides “micro” rest breaks for the most-used body parts
Task done by opposite side of the body

## Slide 34: Lowering Cumulative Trauma Risk Recover from Repetitive Tasks during Work
When possible, create ways to spread out high-demand activities among other required tasks
Intermixing easier physical work within higher-effort tasks provides more opportunities for rest

## Slide 35: Lowering Cumulative Trauma Risk Other Ways
Prepare for job tasks, by warming up your body
  Back: Do you bend, lift, push, pull?
  Arms: Do you reach?
  Hands: Do you grip, type, perform rapid movements?
L
L
L
L
L
L
L
L
L

## Slide 36: Lowering Cumulative Trauma Risk Other Ways
Communicate your job improvement ideas to others you work with
L
L
L
L
L
L
Supervisor
Coworkers
As a young or newly hired employee, you may notice ways to make the work easier that longer-term employees have not considered

## Slide 37: Lowering Cumulative Trauma Risk As a Young Employee…
Do not be afraid to ask questions about job
  Obvious risks to others may not be obvious to you
Find a more-senior employee to provide guidance
  They can offer job tips not covered in training
Reduce exposure to possible distractions
  Working safely may require more attention than you are used to
?
L
STOP
talk
TALK
Talk

## Slide 38: Lowering Cumulative Trauma Risk As a Newly Hired Employee…
Be clear about all workplace safety risks
  Supervisor might assume you know these from past jobs
Report discomfort / pain that does not go away
  New-hires often do more physically demanding jobs
Be sure you fully understand all safety signs and rules
  Are they provided in your preferred language?

## Slide 39: Take-Home Messages

## Slide 40: What to Remember
Young and newly hired employees are at an increased risk of injury when starting a new job
Cumulative trauma from work can cause injuries that are painful and long-lasting
Most cumulative trauma injuries have recognizable symptoms and should be reported
All employees have the ability to use work techniques that reduce their injury risk